## Slide 1: Computer Architecture Project Team A
Sergio Rico, Ertong Zhang,
Vlad Chiriacescu, ZhongYin Zhang

## Slide 2: Outline
Introduction
Motivation
Experimental Protocol
Results

## Slide 3: Introduction
We implement a pipelined 32-bit RISC processor with forwarding mechanism, controller hazards, and instruction & data caches.
Using Quartus II supporting VHDL to conduct the hardware design on Altera’s DE-2 board.
Using assembler to implement a bubble sort program for software components.

## Slide 4: Motivation
Help us master the fundamental ideas of computer architecture and put them into the practice.
Familiar with practical hardware & software co-design methodologies for computer architecture.

## Slide 5: Experimental Protocol
RISC Instruction Set Architecture
Single Cycle Processor Data Path
Pipelines
Hazards
Forwarding
Static Branch Predictor
Caches

## Slide 6: RISC Instruction Set Architecture
3 different assembler codes for bubble sort.
Finally, we choose the best one to our ISA
  Add immediate (addi)
  Load word (lw)
  Set on less than (signed) (slt)
  Branch on equal (beq)
  Store word (sw)

## Slide 7: Single Cycle Processor Data Path

## Slide 8: Single Cycle Processor Data Path
Basic Idea
IFET
CONTROLLER
IDE/WB
MEMORY
EXCUTION

## Slide 9: Pipelines
IF
ID
EX
WB
MEM
Basic Idea of 5 Stages Pipelines

## Slide 10: Pipelines

## Slide 11: Forwarding
Before data is sent to the execution (EXE) stage, the ID stage asks the EXE, DM and WB stages to send their current data.
IF
ID
EX
MEM
WB

## Slide 12: Hazards for LW Instuction
Basic Idea
  We decode the instruction in IF stage, so we can know which instruction is LW (load) in IF stage.
  If the instruction is a load instruction, we add a bubble, even though we do not know whether there is a hazard between this load instruction and the next instruction.
  Therefore the pipeline is stalled for one time. As we are going to send a bubble, we do not need to read instruction next time.

## Slide 13: Branch Predictor
Basic Idea:
  We employed the branch not taken method. If the branch is taken, we introduce a bubble in the pipeline and flush the existing data. We change every output data to be "000...”. In essence, this doesn’t affect the system functioning.

## Slide 14: Caches
Cache Name | Quantity
Block Size | 4*32B
Associativity | 1
Number of blocks in cache | 16
Total | 2KB

## Slide 15: Write Strategy
The write strategy used is write back.
Why we choose Write Back?
  Since the cache is large compared to data required for the given problem, there are not many write backs and this method clearly outperforms a write-through method.

## Slide 16: Results
Our final results including:
  Total Branch Count
  Total Miss predicted Branches
  Instruction Memory Access Count
  Instruction Cache Misses
  Data Memory Access Count
  Data Cache Misses
  Data Cache Write-Backs

## Slide 17: Results

## Slide 18: Thanks